Bottleneck Bandwidth Estimation in SCION

Overview

The Bottleneck Bandwidth is the limiting rate of transfer available between two nodes of a connection on a specific path. This bottleneck can be caused by physical properties of a link such as its physical bandwidth or even by the forwarding mechanisms of a router, such as the time it takes to determine where to forward a packet to. No matter what the cause, the bottleneck bandwidth determines the maximum rate at which data can be sent from source to destination, as all traffic using this path is restricted by the bandwidth that the bottleneck imposes.

In this module, we will use golang to create a simple bottleneck bandwidth estimator in SCION. More specifically, we will implement the packet pair technique. This technique uses the difference in arrival times between two successive packets of the same size in order to provide an estimate of the bandwidth of the connection. Starting with a source that sends two packets of size s each, initially with time interval t0 between them, and being ri ≡ bandwidth = s / ti at link i in the path, we know the following algorithm applies:

tmax = t0
While ri := next_link():
if ri >= (s / tmax):
/* The two packets will never queue because by the time the second packet is
   ready to be transmitted, the first one has already been sent. */
tmax = tmax
Else:
/* The second packet is ready at the link while the first is being still being
   transmitted because of smaller link rate, thus there is queuing. */
tmax = s / ri

More intuitively –see Illustration– when the two packets of size s are sent sequentially close enough (in time), the biggest delay between them will happen at the i-th link, where the bottleneck is, ti = s / ri ti ≥ tj ∀ j (it’s the maximum delay). From this point after passing the i-th node, and by definition, the next delays will not be larger. This means that the destination receives the two packets with an interval tf= ti = s/rbottleneck between them. We know that rbottleneck = s/tf, then knowing s and tf is enough to estimate the bottleneck bandwidth.

Illustration 1: Packets being transmitted (from left to right)

Implementation

Similar to the latency walkthrough, our implementation consists of a sender and a receiver. Let us think of all the factors our estimation relies on and what we are trying to find. To compute rbottleneck , we need s, which is the size of the packet (chosen by us), and we need tf which we can measure.

In order to measure tf, we need to send a sequence of packets, keeping track of when each one was seen at the receiver. In addition, we also want to make sure we deal only with packets part of the test. For this we will use some type of IDs or timestamps.

Task 1: Implement server and client bottleneck bandwidth estimators using the packet pair technique. You may use the suggested implementations below or come up with your own solution. Use the bottleneck bandwidth equation above.

Implementation Proposal: One possible implementation proposes that each packet is sent in an interval, with its own unique identifier, timestamped at the receiver who then returns the timestamp and the identifier for verification. In this way, all calculations and logic can be performed at the source and the server just receives and responds to requests.

Since there exists a bandwidth estimator implemented (see reference [1]) for SCION, you can use it to first estimate the bandwidth and check your results. Also, this implementation is helpful to discover the relevant library calls. Do not use this implementation as a reference as it uses a different approach.
Packet Pair Evaluation

You may notice that results may vary and many may not even make sense, such as if you receive a bandwidth greater than the one that you sent out. This could be because of a number of reasons: how the code is being run and processed, the path the packets take, as well as some key assumptions made about our simplified packet pair technique.
- What assumptions are made when implementing the packet pair technique that could alter the results? Hint: Think of packet queuing, processing, and potential network errors.

Other assumptions, as well as some filtering techniques, can be found on https://www.usenix.org/legacy/publications/library/proceedings/usits01/full_papers/lai/lai_html/node2.html and  by searching online. You are encouraged, but not required, to try to explore how you may adjust these parameters, estimations, and assumptions in order to get more accurate and consistent bandwidth estimation results.

Expansion - SCION’s Impact

Although SCION’s impact on bottleneck bandwidth estimation does not solve the problems introduced by the assumptions above, it can indeed give more insight into the available rate between two nodes through forwarding path control. Since the path is encoded into the packet, one would be able to estimate the bottleneck for each path taken, and moreover, under the assumption that all experiments ran under the same conditions, estimate the bandwidth on some individual nodes that exist in several, disjoint paths. More concretely, since bw(path) = min(bw(node0), bw(node1), ... , bw(nodeN)) for a given path, we could find which node is the bottleneck by enumerating the paths and using the intersections as an estimation.

Task 2: Expand your previous server and client bottleneck bandwidth estimators to not only report the bottleneck bandwidth but the specific path(s) and the node/link causing this bottleneck.

Conclusion

Overall, in this module we have used the Packet Pair technique to implement bottleneck bandwidth estimator applications in SCION that are able to not only report the bottleneck bandwidth between two nodes, but also the paths and nodes that have this bottleneck. We have discussed how SCION is advantageous in this application due to its transparency and control over forwarding paths. In addition, we also discussed the limitations of the Packet Pair technique and the assumptions for its execution. Some improvement of these applications could be achieved via filtering techniques to eliminate noisy measurements.

References

[1] SCION bwtester: https://netsec-ethz.github.io/scion-tutorials/sample_projects/bwtester/
[2] Go library code: https://github.com/netsec-ethz/netsec-scion/tree/scionlab/go/lib
[3] SCION protocol dissector: https://netsec-ethz.github.io/scion-tutorials/scion_tricks/wireshark/
[4] SCION Book (PDF version): https://www.scion-architecture.net/pdf/SCION-book.pdf
[5] SCIONLab: https://www.scionlab.org
[6] SCIONLab Sample Applications: https://github.com/perrig/scionlab/tree/master/
[7] SCIONLab Tutorials: https://netsec-ethz.github.io/scion-tutorials/
[8] SCION Architecture homepage: https://www.scion-architecture.net/